## Slide 1
John Jasa johnjasa@umich.edu
University of Michigan MDO Lab
Justin Gray justin.s.gray@nasa.gov
NASA Glenn Research Center
Getting derivatives in

## Slide 2: This sessions assumes some baseline knowledge
You’ve used OpenMDAO models before
You understand when gradient-based optimization methods are advantageous
You have a working understanding of how to differentiate equations by hand

## Slide 3: Download these slides and tutorial scripts from GitHub
https://github.com/openmdao/openmdao_training
Our materials for today are in the `getting_derivatives_in_openmdao` folder
This repo contains other tutorials to help you get acquainted with OpenMDAO

## Slide 4
Gradient-based optimization with analytic derivatives is our only hope for large-scale problems
100x-10,000x speedup for aerodynamic shape optimization vs. gradient-free1
At least 5x-10x speedup vs. finite-difference2
[1] Lyu et al. ICCFD8-2014-0203
[2] Gray et al. Aviation 2014-2042

## Slide 5: Goals for today
Understand how to obtain partial derivatives for your components
Know the differences between explicit and implicit components and what that means for partials
Briefly learn about some advanced techniques to obtain partial derivatives

## Slide 6: Brief introduction to how OpenMDAO handles derivatives
Why do we need derivatives?
How does OpenMDAO process these derivatives?
How can we efficiently obtain these derivatives?

## Slide 7: Optimization
OpenMDAO is capable of evaluating DOEs and using gradient free methods, but…
Gradient based optimization is A LOT faster!
So we need total derivatives across the whole model:
??

## Slide 8: Finite difference is easy

## Slide 9: Finite difference is easy, but…
Treats your model as a black-box
Expensive
Accuracy can be bad, especially close to the optimal point

## Slide 10: It’s not a good idea to finite difference across solvers
E. S. Hendricks and J. S. Gray, “Pycycle: a tool for efficient optimization of gas turbine engine cycles,” Aerospace, vol. 6, iss. 87, 2019.
E. S. Hendricks, “A multi-level multi-design point approach for gas turbine cycle and turbine conceptual design,” PhD Thesis, 2017.
J. S. Gray, T. A. Hearn, K. T. Moore, J. Hwang, J. Martins, and A. Ning, “Automatic Evaluation of Multidisciplinary Derivatives Using a Graph-Based Problem Formulation in OpenMDAO,” in 15th AIAA/ISSMO Multidisciplinary Analysis and Optimization Conference, 2014.
J. S. Gray, K. T. Moore, T. A. Hearn, and B. A. Naylor, “Standard Platform for Benchmarking Multidisciplinary Design Analysis and Optimization Architectures,” AIAA Journal, vol. 51, iss. 10, p. 2380–2394, 2013.
C. Marriage and Martins, J. R. R. A. “Reconfigurable Semi-Analytic Sensitivity Methods and MDO Architectures Within the πMDO Framework”, in Proceedings of the 12th AIAA/ISSMO Multidisciplinary Analysis and Optimization Conference, Victoria, BC, 2008.
Seriously… don’t do this unless you really have to.
It’s expensive (you have to make your solver tolerances really tight)
It’s inaccurate
It will probably make your optimization converge slowly!
Lots of papers on this topic:

## Slide 11: Complex step is more accurate than FD, but…
Treats your models as a gray-box (might require code modification)
Even more expensive than FD
Some functions are tricky…
  min(), max(), abs() can cause issues
[Martins et al., ACM TOMS, 2003]

## Slide 12: Analytic derivatives are both fast and accurate!

## Slide 13: What about models with coupling?

## Slide 14: How do you differentiate through this convergence loop?
We’ll need a nonlinear solver to converge this coupling.
The solver loop changes the way you compute analytic derivatives

## Slide 15: Manually computing analytic derivatives for coupled models takes a lot of work

## Slide 16: How do compute these extra terms?
These terms will be computed using adjoints!

## Slide 17: When models get really big … have fun!
= ???
Lets be honest, this just isn’t going to happen!

## Slide 18: OpenMDAO can compute these total derivatives for you, automatically!
= [ask OpenMDAO]
For a deep dive on the math:
[Martins and Hwang 2013]
[Hwang and Martins 2018]

## Slide 19: OpenMDAO splits total derivative computation into two steps
Computing the partial derivatives for each component
Solving a linear system for total derivatives

## Slide 20: OpenMDAO splits total derivative computation into two steps
Computing the partial derivatives for each component
  Numerical approach: FD/CS
  Analytic approach: hand derivation or algorithmic differentiation
  Mix and match numerical and analytic
You are responsible for this step, but OpenMDAO can help you a bit

## Slide 21: OpenMDAO splits total derivative computation into two steps
1) Computing the partial derivatives for each component
2) Solving a linear system for total derivatives OpenMDAO does this automatically using a library of different linear solvers for different problems

## Slide 22: By using OpenMDAO’s analytic derivative functionality you can
Efficiently solve optimization problems with 1000’s of design variables or thousands of constraints
Get total derivatives across a complicated model, by providing only partial derivatives of each component
Mix and match different techniques for computing partial derivatives

## Slide 23: Methods for computing derivatives
[Martins and Hwang, AIAA Journal, 2013]
[Martins et al., ACM TOMS, 2003]
Notes: JG: I think you’ll loose people on this slide and its confusing because you have direct and adjoint methods in there, even though you told them “openmdao just does that for you” before.
Here is a quick overview of the different methods that are available.
Finite differences are popular, but suffer from accuracy problems. They are also not efficient, since they require at least one analysis for each design variable.
Only two of them scale well with the number of variables: adjoint methods, and reverse mode AD.

## Slide 24: Computing partial derivatives of an ExplicitComponent
Hand-derived
Sparse hand-derived
Approximated (finite-difference or complex-step)

## Slide 25: ExplicitComponent class
Used for doing explicit calculations
Inputs  Outputs
Can be as simple as a one-line calculation, or as complex as an adjoint CFD solver

## Slide 26: A simple ExplicitComponent example: Calculating lift from CL

## Slide 27: You can analytically compute the partials by hand

## Slide 28: OpenMDAO can approximate partial derivatives for you
Can use the finite-difference or complex-step methods to approximate the partials derivatives
This is generally more computationally expensive than analytic derivatives
It requires very little additional programmer time

## Slide 30
We tell OpenMDAO that all outputs depend on all inputs

## Slide 31: The jacobian is a matrix with one row for each output, and one column for each input

## Slide 32: But each entry in that matrix is really a sub-matrix!
Each input is really a vector
Each output is really a vector
Each entry of the vector is totally separate from all others
So each partial is really a square matrix, with entries only on the diagonal

## Slide 33: But each entry in that matrix is really a sub-matrix!

## Slide 34
Give OpenMDAO the expressions for partial derivatives we computed before
Account for the shape of the Jacobian

## Slide 35: check_partials output
------------------------- Component: ExecComp 'oew' ------------------------- '<output>' wrt '<variable>' | fwd mag. | check mag. | a(fwd-chk) | r(fwd-chk) ------------------------------------------------------------------------------- 'W_empty' wrt 'TOW' | 6.0000e-01 | 6.0000e-01 | 2.3842e-08 | 3.9736e-08 ------------------------------------ Component: BatteryWeight 'batterywt' ------------------------------------ '<output>' wrt '<variable>' | fwd mag. | check mag. | a(fwd-chk) | r(fwd-chk) ----------------------------------------------------------------------------------- 'W_battery' wrt 'LoverD' | 0.0000e+00 | 9.6353e+01 | 9.6353e+01 | 1.0000e+00 >ABS_TOL >REL_TOL 'W_battery' wrt 'TOW' | 0.0000e+00 | 3.2118e-01 | 3.2118e-01 | 1.0000e+00 >ABS_TOL >REL_TOL 'W_battery' wrt 'eta_electric' | 0.0000e+00 | 2.0946e+03 | 2.0946e+03 | 1.0000e+00 >ABS_TOL >REL_TOL 'W_battery' wrt 'eta_prop' | 0.0000e+00 | 2.3218e+03 | 2.3218e+03 | 1.0000e+00 >ABS_TOL >REL_TOL 'W_battery' wrt 'range_desired' | 0.0000e+00 | 1.2847e+01 | 1.2847e+01 | 1.0000e+00 >ABS_TOL >REL_TOL 'W_battery' wrt 'spec_energy' | 0.0000e+00 | 6.4235e+00 | 6.4235e+00 | 1.0000e+00 >ABS_TOL >REL_TOL ---------------------------- Component: WeightBuild 'tow' ---------------------------- '<output>' wrt '<variable>' | fwd mag. | check mag. | a(fwd-chk) | r(fwd-chk) ------------------------------------------------------------------------------- 'TOW' wrt 'W_battery' | 7.5000e+01 | 1.0000e+00 | 7.6000e+01 | 7.6000e+01 >ABS_TOL >REL_TOL 'TOW' wrt 'W_empty' | 7.5000e+01 | 1.0000e+00 | 7.6000e+01 | 7.6000e+01 >ABS_TOL >REL_TOL 'TOW' wrt 'W_payload' | 7.5000e+01 | 1.0000e+00 | 7.6000e+01 | 7.6000e+01 >ABS_TOL >REL_TOL ########################################################### Sub Jacobian with Largest Relative Error: WeightBuild 'tow' ########################################################### '<output>' wrt '<variable>' | fwd mag. | check mag. | a(fwd-chk) | r(fwd-chk) ------------------------------------------------------------------------------- 'TOW' wrt 'W_battery' | 7.5000e+01 | 1.0000e+00 | 7.6000e+01 | 7.6000e+01

## Slide 36: Since each partial is diagonal, we don’t actually need to provide all those 0’s

## Slide 37
Tell OpenMDAO about the sparsity pattern of the Jacobian

## Slide 38
Now our expected partials shapes are vectors, because we’re just giving the non-zero entries to the matrix

## Slide 39: What if we’re too lazy to compute the partials by hand? 

## Slide 40
OpenMDAO can approximate derivatives automatically. Just note that they will be dense!

## Slide 41: Rules of thumb for computing partials
Fine to start out with FD partials while getting your model set up!
For cheap black-box codes:
  FD might be ok for production runs
  CS is better if you can do it!
For “expensive” codes (anything with an internal solver):
  Implement as ImplicitComponent (expose the states/residuals to OpenMDAO)
  Can still FD the residual if you need to
  Analytic derivatives typically cost a lot for these components

## Slide 42: Computing partial derivatives of an ImplicitComponent
Can use the same techniques to obtain partials as explicit
Compute the partials of the residuals with respect to the inputs and outputs

## Slide 43: When do we need to use implicit components?
http://openmdao.org/twodocs/versions/latest/advanced_guide/implicit_comps/defining_icomps.html
For computations where there is not an explicit analytic solution
  y is a state and x,z are inputs
  CFD or FEA analyses
The states are your outputs and you compute residuals for them instead of their analytic solution
Implicit components always require a solver

## Slide 44: Implicit components can use any of the derivative techniques described previously
Hand derived analytic partials (sparse or dense!)
Finite-difference or complex-step dense approximations

## Slide 45: Example implicit component: Aircraft in flight equilibrium
[Falck et al., AIAA SciTech, 2017]

## Slide 46
Define residuals (i.e. the values we want to drive to 0)

## Slide 47
Compute partial derivatives of the residuals wrt the inputs

## Slide 48: Further code example and explanation

## Slide 49: Advanced topics related to obtaining derivatives
Coloring, scaling, etc

## Slide 50: Getting system derivatives efficiently: automatic Jacobian coloring
http://openmdao.org/twodocs/versions/latest/features/core_features/working_with_derivatives/simul_derivs.html

## Slide 51: Show coloring examples

## Slide 52: Show coloring examples

## Slide 53: Getting system derivatives efficiently: automatic Jacobian coloring

## Slide 54
Can use partial derivative coloring to speed up approximation time