## Slide 1
John Jasa johnjasa@umich.edu
Shamsheer Chauhan sschau@umich.edu
Joaquim RRA Martins jrram@umich.edu
University of Michigan MDO Lab
Getting started with

## Slide 2: Download these slides and tutorial scripts from GitHub
https://github.com/johnjasa/openmdao_training

## Slide 3: Levels of expertise suggested to use OpenMDAO
Chart: 
| Python | Optimization and solver setup | Model physics | Math theory
Series 1 | 2.5 | 2 | 1 | 1

## Slide 4: Levels of expertise suggested to use OpenMDAO fluently
Chart: 
| Python | Optimization and solver setup | Model physics | Math theory
Series 1 | 3.5 | 4 | 5 | 2

## Slide 5: Acknowledgements
Ben Brelje, PhD candidate at University of Michigan MDO Lab for creating version 0 of this training
Justin Gray, Engineer and team lead of OpenMDAO at NASA Glenn for refining this workshop
NASA ARMD’s TTT Project has supported OpenMDAO development since 2008

## Slide 6: OpenMDAO is an open-source framework for efficient MDAO
Developed and supported a team at NASA Glenn since 2008
Apache 2.0 license is very permissive (no “copyleft”)
Fast enough for high-fidelity, expensive problems but easy enough for cheap conceptual models
Can be used as a framework, or a low level library for building stand alone codes

## Slide 7: OpenMDAO is a reasonable choice for a wide array of MDAO problems
High-fidelity aeropropulsive optimization with RANS and CEA
Gray et al, Aeropropulsive Design Optimization of a Turboelectric Boundary Layer Ingestion Propulsion System, AIAA/ISSMO Multidisciplinary Analysis and Optimization Conf., 2018

## Slide 8: OpenMDAO is a reasonable choice for a wide array of MDAO problems
High-fidelity aeropropulsive optimization with RANS and CEA
Medium-fidelity aerostructural optimization (VLM/beam)
Chauhan and Martins. Low-Fidelity Aerostructural Optimization of Aircraft Wings with a Simplified Wingbox Model Using OpenAeroStruct. Proc. of the 6th International Conference on Engineering Optimization, 2018

## Slide 9: OpenMDAO is a reasonable choice for a wide array of MDAO problems
High-fidelity aeropropulsive optimization with RANS and CEA
Medium-fidelity aerostructural optimization (VLM/beam)
Conceptual-fidelity sizing and tradespace exploration
Benjamin J. Brelje and Joaquim R.R.A. Martins. “Development of a Conceptual Design Model for Aircraft Electric Propulsion with Efficient Gradients”, 2018 AIAA/IEEE Electric Aircraft Technologies Symposium

## Slide 10: OpenMDAO is a reasonable choice for a wide array of MDAO problems
Dykes et al., 2015, AIAA SciTech
Chung et al., 2019, SMO
Jasa et al., 2018, AIAA Aviation

## Slide 11: OpenMDAO is a reasonable choice for a wide array of MDAO problems
Hegseth and Bachynski, 2019
Chauhan and Martins, 2019

## Slide 12: Goals for today
Learn enough to run a useful OpenMDAO model
Gain some intuition about the operating theory
Get excited about using analytic derivatives for optimization

## Slide 13: Overview
OpenMDAO intro and basics
  Lab 0: Explicit components and connections
Using solvers with implicit models
  Lab 1: Comparing gradient-free and gradient-based solvers
Optimization with and without analytic derivatives
  Lab 2: Optimizing the thickness distribution of a simple beam
Wrapping external codes
  Lab 3: Wrapping external codes as explicit and implicit components

## Slide 14: OpenMDAO intro and Basics
Intro and terminology
Building explicit components and connecting them together
Lab 0: Implementing a simple explicit calculation (Breguet Range)

## Slide 15: OpenMDAO has nice features
Units
  Conversions
  (In)compatibility checks

## Slide 16: OpenMDAO has nice features
Units
  Conversions
  (In)compatibility checks
Automatic checks for unconnected inputs

## Slide 17: OpenMDAO has nice features
Units
  Conversions
  (In)compatibility checks
Automatic checks for unconnected inputs
Interactive N2 diagrams

## Slide 18: OpenMDAO has nice features
Units
  Conversions
  (In)compatibility checks
Automatic checks for unconnected inputs
Interactive N2 diagrams
Models are Python objects (inheritance!)

## Slide 19: OpenMDAO has advanced numerical methods
Efficient solvers for implicit systems
  Newton solver
  Nonlinear block Gauss-Seidel

## Slide 20: OpenMDAO has advanced numerical methods
Efficient solvers for implicit systems
  Newton solver
  Nonlinear block Gauss-Seidel
Derivative computation (for gradient-based opt.)
  Forward and reverse analytic
  Finite difference or complex step
  Mixture of all!

## Slide 21: OpenMDAO has advanced numerical methods
Efficient solvers for implicit systems
  Newton solver
  Nonlinear block Gauss-Seidel
Derivative computation (for gradient-based opt.)
  Forward and reverse analytic
  Finite difference or complex step
  Mixture of all!
MPI parallelization

## Slide 22: OpenMDAO problem hierarchy
Components implement the actual model computation

## Slide 23
Components implement the actual model computation
Groups organize the model and enable hierarchical solver strategies
OpenMDAO problem hierarchy

## Slide 24: OpenMDAO problem hierarchy
Components implement the actual model computation
Groups organize the model and enable hierarchical solver strategies
Drivers iteratively execute the model (optimizers and DOEs)

## Slide 25
Components implement the actual model computation
Groups organize the model and enable hierarchical solver strategies
Drivers iteratively execute the model (optimizers and DOEs)
Problem is the top-level container
OpenMDAO problem hierarchy

## Slide 26
Convenient containers of data and methods
It allows inheritance of features
Can reuse component and group templates easily
Why use classes in object-oriented programming?

## Slide 27: ExplicitComponent class
Used for doing explicit calculations
Inputs  Outputs
Can be as simple as a one-line calculation, or as complex as an adjoint CFD solver

## Slide 28: ExplicitComponent example

## Slide 29: ExplicitComponent example
All your model components will subclass OpenMDAO base classes

## Slide 30: ExplicitComponent example
Define any options / run flags which do not change during evaluation

## Slide 31: ExplicitComponent example
Define model inputs, output, and (optionally) partial derivs using the setup() method. Called once before solve / optimization

## Slide 32: ExplicitComponent example
Do the actual computation using compute(). Need to fill in values for all your declared outputs by the end of this method. Called every time the model is evaluated

## Slide 33: ExplicitComponent example
Variable name
Default value (before model runs)
Units (need not match upstream)
Human-readable description (optional)
Will default to expecting user provided analytic derivatives, but we can specify `fd` later…
Variable dimension
(in this case, a n x 1 vector)

## Slide 34: IndepVarComp example
IndepVarComps only have only outputs; they do not take in any input variables
IVCs are used in an optimization context to allow the optimizer to control design variables
indeps = self.add_subsystem('indeps', om.IndepVarComp())
indeps.add_output(‘h’, 10000, units=“ft“)
indeps.add_output(‘U’, 200, units=“kn")
indeps.add_output(‘Sref', 200, units=“ft**2”)

## Slide 35: Groups: organizing components
Combine components into a Group to build organized models
Groups can hold other Groups, which allows hierarchal solution strategies
Groups can used to create portable chunks of analysis chains

## Slide 36: Grouping components
Define a model by subclassing Group
indeps
atmos
lift
Sref
U
h
rho
This is the model structure that is being connected

## Slide 37: Grouping components
Include components using the add_subsystem(<name>, <component>) method
Python note:
These are instances of a component class

## Slide 38: Grouping components
Your custom components can be defined in the same .py file, or imported from a package for modularity
Specify flags/options now

## Slide 39: Grouping components
Connect parameters using the connect(<from>, <to>) method
indeps
atmos
lift
Sref
U
h
rho

## Slide 40: Grouping components
Note the namespace / address string:
component_name.variable

## Slide 41: Grouping components
When you run an MDA/MDO problem, you will add one top-level Group instance to the problem

## Slide 42: Another way to connect…
If parameters are widely used among many components, writing many connect() statements can be tedious
Variable promotion is another way to make connections

## Slide 43: What does variable promotion do?
Creates an alias for the variable one level up in the namespace
  (atmos.h  h)
  (lift.rho  rho)
Automatically connects any matching I/O variable names
Promote variables with wildcard (e.g. *_in or just *)

## Slide 44: What does variable promotion do?
Input/output connection established automatically
indeps
atmos
lift
Sref
U
h
rho

## Slide 45: What does variable promotion do?
Multiple promoted outputs with same name: not allowed (will raise an exception)

## Slide 46: What does variable promotion do?
Multiple promoted inputs with identical name: OK and encouraged
(all connections automatically made)

## Slide 47: What does variable promotion do?
Mixing promotion with connect statements:
allowed / appropriate

## Slide 48: Lab 0: Implementing simple explicit calculations (Breguet Range)
Step 1: Install OpenMDAO
Step 2: Write your first component
Step 3: World domination!

## Slide 49: Lab 0.a: Install
Open cmd prompt
Internet install: pip install openmdao
Local Install:
  cd to wherever OpenMDAO is downloaded: `pip install .`(note the period)
  This installs from local source files, not PyPI
cd ../openmdao_training
python paraboloid.py
  If this works without error, your installation should be good

## Slide 50: Lab 0.b: Aircraft Range
Open lab_0_template.py in a text editor or IDE and rename it to lab_0.py
The BreguetRange component implements the electric Breguet equation:
Your goal is to compute the maximum range of an airplane given a certain payload

## Slide 51: Lab 0.b: Aircraft Range
Complete the TODOs in the BatteryWeight component
Complete the TODOs in the ElecRangeGroup definition by connecting the two components
cd into project folder to check and run the model:
  openmdao view_model lab_0.py (creates model diagram)
  python lab_0.py (runs the model)
Answer key in the lab_0_solution.py file (don’t cheat!)

## Slide 52: Lab 0.b: Aircraft Range
openmdao view_model lab_0.py
If you forgot any connections, you’ll see some red
All the red boxes represent unconnected inputs to components. Use explicit connection or variable promotion to get rid of all the red

## Slide 53: Lab 0.b: The n2 is your best friend!
Model hierarchy (groups,
components, variables)
Inside a box is within a single component
Connections!
Linear and nonlinear solver hierarchy
(more on this later…)

## Slide 54: Lab 0.b: Aircraft Range
N2 diagram is upper-triangular:
Pure explicit computation (feed-forward)
It should look like this!
This diagram is interactive:
Right click on the components/groups to collapse and expand them
Click on any black colored square to trace connections between components

## Slide 55: Lab 0 summary:
Everything we just did we can do faster in Excel.
This is a tutorial so the models are extremely simple and cheap, but …
Real-world models have hierarchies of dozens or hundreds of logical components
Real-world models often lack a closed form solution and require some kind of solver or iteration strategy

## Slide 56: Using solvers with implicit models
Gradient-free solver: Nonlinear Block Gauss-Seidel (i.e. Fixed point iteration)
Gradient-based solver: Newton’s Method
Lab 1: Simple aircraft sizing and experimenting with different solver algorithms

## Slide 57: OpenMDAO Nonlinear Solvers
When a circular dependency is detected, OpenMDAO needs a solver to converge the problem:
Choice #1: NonlinearBlockGS()
Choice #2: NewtonSolver()
Choice #3: BroydenSolver()
Choice #4: NonlinearBlockJac()

## Slide 58: Check out the docs for more info!
Look at the docs for OpenMDAO’s standard library:
Lots of details on all the different solvers!

## Slide 59: Check out the docs for more info!
Look at the docs for OpenMDAO’s standard library:
Lots of details on all the different solvers!
Also see sections for surrogates and helpful general purpose components!

## Slide 60: Nonlinear Block Gauss-Seidel (Deriv Free)
Model 1
Model 2
Model 3
Cycle connection

## Slide 61: Nonlinear Block Gauss-Seidel
Model 1
Model 2
Model 3
Cycle connection
Run Model 1, give outputs to Model 2

## Slide 62: Nonlinear Block Gauss-Seidel
Model 1
Model 2
Model 3
Cycle connection
Run Model 2, give outputs to Model 3

## Slide 63: Nonlinear Block Gauss-Seidel
Model 1
Model 2
Model 3
Cycle connection
Run Model 3, give outputs to Model 1

## Slide 64: Nonlinear Block Gauss-Seidel
Model 1
Model 2
Model 3
Cycle connection
Run Model 1, give outputs to Model 2

## Slide 65: Nonlinear Block Gauss-Seidel
Model 1
Model 2
Model 3
Cycle connection
Run Model 2, give outputs to Model 3

## Slide 66: Newton’s Method is simple in one dimension (Requires derivs)

## Slide 67: Newton Solver for multiple dimensions is a bit more complex
We want to drive residuals to 0
x: design variables
y: implicit state variables
Do a Taylor series with respect to the current point
We want residuals to be 0 at the next iteration y + dy
Solve for dy that would drive the linearize residuals to 0
Solve this linear system
Then take a step. Repeat until converged
ny
ny
ny
1
1
=

## Slide 68: Newton Solver needs some partial derivatives!
ny
ny
ny
1
1
=

## Slide 69: Partial Derivatives in OpenMDAO
OpenMDAO assembles the Jacobian for you, from provided component partials
Define analytic derivatives:
partials(<of>, <with respect to>)
This tells OpenMDAO which partials exist
This tells OpenMDAO the actual values of the partials

## Slide 70: Lab # 1 : Aircraft Sizing
Next, we will “size” an electric aircraft for desired range
Open lab_1_template.py in a text editor or IDE and rename lab_1.py
Check the model by building an N2 diagram
This system is implicit (because it has a cycle) but has no implicit components

## Slide 71: Lab # 1 : Aircraft Sizing
Run the model as-is using NLBGS (python lab_1.py)
  The numbers that print out are the absolute and relative residuals
Change the empty weight fraction to 0.55
  check out the ExecComp
Try using the Newton solver (~ Line 124). What happens?
  Check your partial derivatives (~ Line 173)
  Fix the partial derivatives of the incorrect components
  Which solver uses fewer iterations?
Print all the inputs and outputs (~ Line 178, 179)

## Slide 72: check_partials output
------------------------- Component: ExecComp 'oew' ------------------------- '<output>' wrt '<variable>' | fwd mag. | check mag. | a(fwd-chk) | r(fwd-chk) ------------------------------------------------------------------------------- 'W_empty' wrt 'TOW' | 6.0000e-01 | 6.0000e-01 | 2.3842e-08 | 3.9736e-08 ------------------------------------ Component: BatteryWeight 'batterywt' ------------------------------------ '<output>' wrt '<variable>' | fwd mag. | check mag. | a(fwd-chk) | r(fwd-chk) ----------------------------------------------------------------------------------- 'W_battery' wrt 'LoverD' | 0.0000e+00 | 9.6353e+01 | 9.6353e+01 | 1.0000e+00 >ABS_TOL >REL_TOL 'W_battery' wrt 'TOW' | 0.0000e+00 | 3.2118e-01 | 3.2118e-01 | 1.0000e+00 >ABS_TOL >REL_TOL 'W_battery' wrt 'eta_electric' | 0.0000e+00 | 2.0946e+03 | 2.0946e+03 | 1.0000e+00 >ABS_TOL >REL_TOL 'W_battery' wrt 'eta_prop' | 0.0000e+00 | 2.3218e+03 | 2.3218e+03 | 1.0000e+00 >ABS_TOL >REL_TOL 'W_battery' wrt 'range_desired' | 0.0000e+00 | 1.2847e+01 | 1.2847e+01 | 1.0000e+00 >ABS_TOL >REL_TOL 'W_battery' wrt 'spec_energy' | 0.0000e+00 | 6.4235e+00 | 6.4235e+00 | 1.0000e+00 >ABS_TOL >REL_TOL ---------------------------- Component: WeightBuild 'tow' ---------------------------- '<output>' wrt '<variable>' | fwd mag. | check mag. | a(fwd-chk) | r(fwd-chk) ------------------------------------------------------------------------------- 'TOW' wrt 'W_battery' | 7.5000e+01 | 1.0000e+00 | 7.6000e+01 | 7.6000e+01 >ABS_TOL >REL_TOL 'TOW' wrt 'W_empty' | 7.5000e+01 | 1.0000e+00 | 7.6000e+01 | 7.6000e+01 >ABS_TOL >REL_TOL 'TOW' wrt 'W_payload' | 7.5000e+01 | 1.0000e+00 | 7.6000e+01 | 7.6000e+01 >ABS_TOL >REL_TOL ########################################################### Sub Jacobian with Largest Relative Error: WeightBuild 'tow' ########################################################### '<output>' wrt '<variable>' | fwd mag. | check mag. | a(fwd-chk) | r(fwd-chk) ------------------------------------------------------------------------------- 'TOW' wrt 'W_battery' | 7.5000e+01 | 1.0000e+00 | 7.6000e+01 | 7.6000e+01

## Slide 73: Lab # 1 : Aircraft Sizing continued
Switch back to the Gauss-Seidel solver
Switch to the WeightBuildImplicit component
  solves for TOW by forcing design range equal to analyzed range
  What happens when you run the model? Why?
  Try the Newton solver

## Slide 74: Optimization with and without analytic derivatives
High level introduction to different methods of computing derivatives
Lab 2: Optimization of a FEM for a cantilever beam

## Slide 75: Optimization
OpenMDAO is capable of evaluating DOEs just like ModelCenter, but…
Gradient based optimization is A LOT faster!
So we need total derivatives across the whole model:
??

## Slide 76: Finite difference is easy

## Slide 77: Finite difference is easy, but…
Treats your model as a black-box
Expensive
Accuracy can be bad, especially close to the optimal point

## Slide 78: It’s not a good idea to finite difference across solvers
E. S. Hendricks and J. S. Gray, “Pycycle: a tool for efficient optimization of gas turbine engine cycles,” Aerospace, vol. 6, iss. 87, 2019.
E. S. Hendricks, “A multi-level multi-design point approach for gas turbine cycle and turbine conceptual design,” PhD Thesis, 2017.
J. S. Gray, T. A. Hearn, K. T. Moore, J. Hwang, J. Martins, and A. Ning, “Automatic Evaluation of Multidisciplinary Derivatives Using a Graph-Based Problem Formulation in OpenMDAO,” in 15th AIAA/ISSMO Multidisciplinary Analysis and Optimization Conference, 2014.
J. S. Gray, K. T. Moore, T. A. Hearn, and B. A. Naylor, “Standard Platform for Benchmarking Multidisciplinary Design Analysis and Optimization Architectures,” AIAA Journal, vol. 51, iss. 10, p. 2380–2394, 2013.
C. Marriage and Martins, J. R. R. A. “Reconfigurable Semi-Analytic Sensitivity Methods and MDO Architectures Within the πMDO Framework”, in Proceedings of the 12th AIAA/ISSMO Multidisciplinary Analysis and Optimization Conference, Victoria, BC, 2008.
Seriously… don’t do this unless you really have to.
It’s expensive (make your solver tolerances really tight)
It’s inaccurate
It will probably make your optimization converge slowly!
Lots of papers on this topic:

## Slide 79: Complex step is more accurate than FD, but…
Treats your models as a gray-box (might require code modification)
Even more expensive
Some functions are tricky…
  min(), max(), abs() can cause issues

## Slide 80: Analytic derivatives are both fast and accurate!

## Slide 81: What about models with coupling?

## Slide 82: How do you differentiate through this convergence loop?
We’ll need a nonlinear solver to converge this coupling.
The solver loop changes the way you compute analytic derivatives

## Slide 83: Manually computing analytic derivatives for coupled models takes a lot of work

## Slide 84: How do compute these extra terms?
These terms will be computed using adjoints!

## Slide 85: When models get really big … have fun!
= ???
Lets be honest, this just isn’t going to happen!

## Slide 86: OpenMDAO can compute these total derivatives for you, automatically!
= [ask OpenMDAO]
For a deep dive on the math:
[Martins and Hwang 2013]
[Hwang and Martins 2018]

## Slide 87: OpenMDAO splits total derivative computation into two steps
Computing the partial derivatives for each component
Solving a linear system for total derivatives

## Slide 88: OpenMDAO splits total derivative computation into two steps
Computing the partial derivatives for each component
  Numerical approach: FD/CS
  Analytic approach: hand derivation or algorithmic differentiation
  Mix and match numerical and analytic
You are responsible for this step, but OpenMDAO can help you a bit

## Slide 89: OpenMDAO splits total derivative computation into two steps
1) Computing the partial derivatives for each component
2) Solving a linear system for total derivatives OpenMDAO does this automatically using a library of different linear solvers for different problems

## Slide 90: By using OpenMDAO’s analytic derivative functionality you can
Efficiently solve optimization problems with 1000’s of design variables or thousands of constraints
Get total derivatives across a complicated model, by providing only partial derivatives of each component
Mix and match different techniques for computing partial derivatives

## Slide 91: Rules of thumb for computing partials
Fine to start out with FD partials while getting your model set up!
For cheap black-box codes:
  FD might be ok for production runs
  CS is better if you can do it!
For “expensive” codes (anything with an internal solver):
  Implement as ImplicitComponent (expose the states/residuals to OpenMDAO)
  Can still FD the residual if you need to
  Analytic derivatives typically cost a lot for these components

## Slide 92: Optimization
Optimization is handled by a Driver
add_objective(<var_name>)
add_design_var(<var_name>, lower=…, upper=…)
ScipyOptimizeDriver is what most people will use on Windows
run_driver instead of run_model
add_constraint(<var_name>, lower=…, upper=…)

## Slide 93: Optimization
Available drivers:
ScipyOptimizeDriver will work in Anaconda
  Works on Windows machines
  SLSQP method is the standard constrained opt in OpenMDAO
PyoptSparseDriver is much better (SNOPT algorithm) but really only builds on Linux/MacOSX (hard to build on windows, but technically is possible)

## Slide 94: Recording the optimization history
Often you will want to record variable values changing over the course of an optimization.
This is achieved using a “recorder” object
This will record all the objective, all constraints, and all dvs for each optimizer iteration (but no “intermediate variables”)

## Slide 95: Saving all the variables for the final optimized point
We don’t normally save all the variables for every iteration to avoid making huge database files
This configures a secondary case type to record specific runs with all the variables

## Slide 96: Lab #2: Optimization of a cantilever beam
Find the thickness distribution for a cantilever beam that minimizes compliance subject to a volume constraint
Check out the other examples on your own!
F

## Slide 97: Lab #2: Simple FEM in 5 steps!
0) Break the beam into segments (0 doesn’t count as a real step!)
Compute the moment of inertia for each segment
Compute the local stiffness matrix for each segment
Combine all the local stiffness matrices into a global K matrix and solve the FEM
Pull displacements from the state vector and compute compliance
Compute beam volume

## Slide 98: Lab #2: Pay close attention to step 4!
0) Break the beam into segments (0 doesn’t count as a real step!)
Compute the moment of inertia for each segment
Compute the local stiffness matrix for each segment
Combine all the local stiffness matrices into a global K matrix and solve the FEM
Pull displacements from the state vector and compute compliance
Compute beam volume
using the src_indices argument to the connect method,
you can extract just the relevant portion of the state vector for the
compliance calculation

## Slide 99: Lab #2: Get to it!
Copy the “lab_2_template.py” file to a new file called “lab_2.py”
Add components in the correct order (~ line 40)
Connect the components together (~line 48)
Use the N2 diagram to make sure you have everything connected (no red inputs!)
What happens if you switch to full model FD? Does it work? Try changing the FD step size…
What about CS?
How does compute cost scale with num_elements for different methods of computing derivatives?

## Slide 100: Wrapping external codes
How to handle file wrappers with OpenMDAO’s built in helper components
Lab 3: Explicit and Implicit file wrappers

## Slide 101: OpenMDAO has two file wrapper components in the standard library
There are lots of useful components
In the standard library!
spines, constraint aggregation,
file wrappers, Ax=b, Ax, etc…
Have a look through these comps,
So you know whats there

## Slide 102: ExternalCodeComp
Inherit from OpenMDAO provided class
Define the I/O like normal
Wrapper specific options
Write the input file
Create a sub-process to run the code
Parse the output file
Push the values back into
OpenMDAO’s output vector

## Slide 103: ExternalCodeImplicitComp
Inherit from OpenMDAO provided class
(different base class then for the explicit case!)
Define the I/O like normal
apply_nonlinear is the
Residual evaluation
Write the input file
Create a sub-process to run the code
Parse the output file
Wrapper specific options
solve_nonlinear asks the
code to converge itself using
its own internal solvers

## Slide 104: Lab #3: Beam optimization with file wrapped external codes
cd into the `lab_3` folder
Have a quick look at standalone_beam.py this is a pure python version of the same FEM you built in OpenMDAO for Lab #2 (but without derivatives)
Call `python standalone_beam.py opt` from the command line
Call `python lab_3_explicit_wrapper.py`
Call `python lab_3_implicit_wrapper.py`
Why does the implicit wrapper call both solve_nonlinear and apply_nonlinear? (hint: it has to do with derivatives)
Compare the compute cost of running the optimization using pure OpenMDAO, the standalone optimization, and the file wrapped version.

## Slide 105: Advanced Topics
Model architecting
Vectorization
Implicit components
Getting system derivatives efficiently
High-fidelity and expensive tools
Debugging tools and processes
Surrogate modeling
Trajectory optimization
Propulsion analysis

## Slide 106: Model architecting
Developing good OpenMDAO models is like object-oriented software engineering: you need to pick the right level to draw the component boundary
In my opinion, a good component has:
  on the order of 5 – 20 inputs
  1 – 20 outputs
  a few computations that are logically related
Python’s package import system makes this easy
Real-world examples:
https://github.com/mdolab/OpenConcept
https://github.com/mdolab/OpenAeroStruct

## Slide 107: Model architecting example

## Slide 108: Vectorization
Where possible, avoid instantiating models over and over for multi-point analyses (e.g. trajectory optimization)
Instead, do vectorized computations using numpy
OpenMDAO needs to know the dimension of all component inputs / outputs at setup() time
  Best practice: pass in vector length as a self.option[‘vec_size’]
  If you mess this up you’ll get dimension mismatch errors at run time

## Slide 109: Vectorization
shape=(dim1, dim2,…)
User sets vector dims when instantiating the model
Sparse Jacobian indices for vector input and vector output
Sparse Jacobian indices for scalar input and vector output

## Slide 110: Vectorization
Many flight conditions computed at once using vectorized computation

## Slide 111: Implicit Components
http://openmdao.org/twodocs/versions/latest/advanced_guide/implicit_comps/defining_icomps.html
Useful for computations where there isn’t an easily written explicit expression
  y is a state and x,z are inputs
  CFD or FEA analyses
You compute the residuals for the states instead of the outputs directly
Implicit components always require a solver

## Slide 112: Getting system derivatives efficiently: automatic Jacobian coloring
http://openmdao.org/twodocs/versions/latest/features/core_features/working_with_derivatives/simul_derivs.html

## Slide 113: Getting system derivatives efficiently: automatic Jacobian coloring

## Slide 114: High-fidelity and expensive tools
OpenMDAO can handle a mix of fidelity levels easily
Can parallelize at the group or subgroup level
Only requiring the partial derivatives becomes quite important here

## Slide 115: High-fidelity and expensive tools

## Slide 116
[Hwang et al., AIAA 2019-1.C035082]
High-fidelity and expensive tools

## Slide 117: High-fidelity and expensive tools

## Slide 118: Debugging tools
Many tools come pre-packaged in OpenMDAO to help you develop, debug, and run your models
  N2
  Connection viewer
  Speed and memory profiling
  Call tracing
http://openmdao.org/twodocs/versions/latest/other/om_command.html

## Slide 119: Connection viewer

## Slide 120: Speed and memory profiling

## Slide 121: Call tracing

## Slide 122: Surrogate modeling
Built-in methods for structured and unstructured data interpolation
  Kriging surrogate
  Nearest neighbor
  Response surface
http://openmdao.org/twodocs/versions/latest/features/building_blocks/components/metamodelunstructured_comp.html

## Slide 123: Surrogate modeling

## Slide 124: Trajectory optimization: Dymos
Dymos is a tool built using OpenMDAO that solves optimal control problems involving multidisciplinary system
Example optimal trajectory for an aircraft climb shown on right
http://github.com/openmdao/dymos

## Slide 125: Propulsion optimization: PyCycle
E. S. Hendricks and J. S. Gray, “Pycycle: a tool for efficient optimization of gas turbine engine cycles,” Aerospace, vol. 6, iss. 87, 2019.
https://github.com/openmdao/pycycle

## Slide 126: Thank you!