## Slide 1
John Jasa johnjasa@umich.edu
Shamsheer Chauhan sschau@umich.edu
University of Michigan MDO Lab
Getting started with A tutorial / workshop

## Slide 2: Download these slides and tutorial scripts from GitHub
https://github.com/johnjasa/openmdao_training

## Slide 3: Acknowledgements
Ben Brelje, PhD candidate at University of Michigan MDO Lab for creating version 0 of this training
Justin Gray, Engineer and team lead of OpenMDAO at NASA Glenn for refining this workshop
NASA ARMD’s TTT Project has supported OpenMDAO development since 2008

## Slide 4: OpenMDAO is an open-source framework for efficient MDAO
Developed and supported a team at NASA Glenn since 2008
Apache 2.0 license is very permissive (no “copyleft”)
Fast enough for high-fidelity, expensive problems but easy enough for cheap conceptual models
Can be used as a framework, or a low level library for building stand alone codes

## Slide 5: OpenMDAO is a reasonable choice for a wide array of MDAO problems
High-fidelity aeropropulsive optimization with RANS and CEA
Gray et al, Aeropropulsive Design Optimization of a Turboelectric Boundary Layer Ingestion Propulsion System, AIAA/ISSMO Multidisciplinary Analysis and Optimization Conf., 2018

## Slide 6: OpenMDAO is a reasonable choice for a wide array of MDAO problems
High-fidelity aeropropulsive optimization with RANS and CEA
Medium-fidelity aerostructural optimization (VLM/beam)
Chauhan and Martins. Low-Fidelity Aerostructural Optimization of Aircraft Wings with a Simplified Wingbox Model Using OpenAeroStruct. Proc. of the 6th International Conference on Engineering Optimization, 2018

## Slide 7: OpenMDAO is a reasonable choice for a wide array of MDAO problems
High-fidelity aeropropulsive optimization with RANS and CEA
Medium-fidelity aerostructural optimization (VLM/beam)
Conceptual-fidelity sizing and tradespace exploration
Benjamin J. Brelje and Joaquim R.R.A. Martins. “Development of a Conceptual Design Model for Aircraft Electric Propulsion with Efficient Gradients”, 2018 AIAA/IEEE Electric Aircraft Technologies Symposium

## Slide 8: OpenMDAO is a reasonable choice for a wide array of MDAO problems
Dykes et al., 2015, AIAA SciTech
Chung et al., 2019, SMO
Jasa et al., 2018, AIAA Aviation

## Slide 9: Goals for today
Learn enough to run a useful OpenMDAO model
Gain some intuition about the operating theory
Get really excited about using analytic derivatives for optimization!

## Slide 10: Overview
OpenMDAO intro and basics
  Lab 0: Explicit components and connections
Using solvers with implicit models
  Lab 1: Comparing gradient-free and gradient-based solvers
Optimization with and without analytic derivatives
  Lab 2: Optimizing the thickness distribution of a simple beam
Wrapping external codes
  Lab 3: Wrapping external codes as explicit and implicit components

## Slide 11: OpenMDAO intro and Basics
Intro and terminology
Building explicit components and connecting them together
Lab 0: Implementing a simple explicit calculation (Breguet Range)

## Slide 12: OpenMDAO has nice features
Units
  Conversions
  (In)compatibility checks

## Slide 13: OpenMDAO has nice features
Units
  Conversions
  (In)compatibility checks
Automatic checks for unconnected inputs

## Slide 14: OpenMDAO has nice features
Units
  Conversions
  (In)compatibility checks
Automatic checks for un-connected inputs
Interactive N2 diagrams

## Slide 15: OpenMDAO has nice features
Units
  Conversions
  (In)compatibility checks
Automatic checks for un-connected inputs
Interactive N2 diagrams
Models are Python objects (inheritance!)

## Slide 16: OpenMDAO has best-in-class numerical methods
Efficient solvers for implicit systems
  Newton solver
  Nonlinear block Gauss-Seidel

## Slide 17: OpenMDAO has best-in-class numerical methods
Efficient solvers for implicit systems
  Newton solver
  Nonlinear block Gauss-Seidel
Derivative computation (for gradient-based opt.)
  Forward and reverse analytic
  Finite difference or complex step
  Mixture of all!

## Slide 18: OpenMDAO has best-in-class numerical methods
Efficient solvers for implicit systems
  Newton solver
  Nonlinear block Gauss-Seidel
Derivative computation (for gradient-based opt.)
  Forward and reverse analytic
  Finite difference or complex step
  Mixture of all!
MPI parallelization

## Slide 19: OpenMDAO architecture
Components implement the actual model computation

## Slide 20
Components implement the actual model computation
Groups organize the model and enable hierarchical solver strategies
OpenMDAO architecture

## Slide 21: OpenMDAO architecture
Components implement the actual model computation
Groups organize the model and enable hierarchical solver strategies
Drivers iteratively execute the model (optimizers and DOEs)

## Slide 22
Components implement the actual model computation
Groups organize the model and enable hierarchical solver strategies
Drivers iteratively execute the model (optimizers and DOEs)
Problem is the top-level container
OpenMDAO architecture

## Slide 23: ExplicitComponent class
Used for doing explicit calculations
Inputs  Outputs with no iteration / implicit states
Can be as simple as a one-line calculation, or as complex as an adjoint CFD solver

## Slide 24: ExplicitComponent example

## Slide 25: ExplicitComponent example
All your model components will subclass OpenMDAO base classes

## Slide 26: ExplicitComponent example
Define any options / run flags which do not change during evaluation

## Slide 27: ExplicitComponent example
Define model inputs, output, and (optionally) partial derivs using the setup() method. Called once before solve / optimization

## Slide 28: ExplicitComponent example
Do the actual computation using compute(). Need to fill in values for all your declared outputs by the end of this method. Called every time the model is evaluated

## Slide 29: ExplicitComponent example
Variable name
Default value (before model runs)
Units (need not match upstream)
Human-readable description (optional)
Will default to expecting user provided analytic derivatives, but we can specify `fd` later…
Variable dimension
(in this case, a n x 1 vector)

## Slide 30: Connecting multiple components
Combine components into a Group to build models
Groups can hold other Groups, forming a hierarchy

## Slide 31: Connecting multiple components
Define a model by subclassing Group
indeps
atmos
lift
Sref
U
h
rho

## Slide 32: Connecting multiple components
Include components using the add_subsystem(<name>, <component>) method
Python note:
These are instances of a component class

## Slide 33: Connecting multiple components
Your custom components can be defined in the same .py file, or imported from a package for modularity
Specify flags/options now

## Slide 34: Connecting multiple components
Connect parameters using the connect(<from>, <to>) method
indeps
atmos
lift
Sref
U
h
rho

## Slide 35: Connecting multiple components
Note the namespace / address string:
component_name.variable

## Slide 36: Connecting multiple components
When you run an MDA/MDO problem, you will add one top-level Group instance to the problem

## Slide 37: Another way to connect…
If parameters are widely used among many components, writing many connect() statements can be tedious
Variable promotion is another way to make connections

## Slide 38: What does variable promotion do?
Creates an alias for the variable one level up in the namespace
  (atmos.h  h)
  (lift.rho  rho)
Automatically connects any matching I/O variable names
Promote variables with wildcard (e.g. *_in or just *)

## Slide 39: What does variable promotion do?
Input/output connection established automatically
indeps
atmos
lift
Sref
U
h
rho

## Slide 40: What does variable promotion do?
Multiple promoted outputs with same name: not allowed (will raise an exception)

## Slide 41: What does variable promotion do?
Multiple promoted inputs with identical name: OK and encouraged
(all connections automatically made)

## Slide 42: What does variable promotion do?
Mixing promotion with connect statements:
allowed / appropriate

## Slide 43: Lab 0: Implementing simple explicit calculations (Breguet Range)
Step 1: Install OpenMDAO
Step 2: Write your first component
Step 3: World domination!

## Slide 44: Lab 0.a: Install
Open cmd prompt
Internet install: pip install openmdao
Local Install:
  cd to wherever OpenMDAO is downloaded: `pip install .`(note the period)
  This installs from local source files, not PyPI
cd ../openmdao_training
python paraboloid.py
  If this works without error, your installation should be good

## Slide 45: Lab 0.b: Aircraft Range
Open lab_0_template.py in a text editor or IDE and rename it to lab_0.py
The BreguetRange component implements the electric Breguet equation:
Your goal is to compute the maximum range of an airplane given a certain payload

## Slide 46: Lab 0.b: Aircraft Range
Complete the TODOs in the BatteryWeight component
Complete the TODOs in the ElecRangeGroup definition by connecting the two components
cd into project folder to check and run the model:
  openmdao view_model lab_0.py (creates model diagram)
  python lab_0.py (runs the model)
Answer key in the lab_0_solution.py file (don’t cheat!)

## Slide 47: Lab 0.b: Aircraft Range
openmdao view_model lab_0.py
If you forgot any connections, you’ll see some red
All the red boxes represent unconnected inputs to components. Use explicit connection or variable promotion to get rid of all the red

## Slide 49: Lab 0.b: Aircraft Range
N2 diagram is upper-triangular:
Pure explicit computation (feed-forward)
It should look like this!
This diagram is interactive:
Right click on the components/groups to collapse and expand them
Click on any black colored square to trace connections between components

## Slide 50: Lab 0 summary:
Everything we just did we can do faster in Excel.
This is a tutorial so the models are extremely simple and cheap, but …
Real-world models have hierarchies of dozens or hundreds of logical components
Real-world models often lack a closed form solution and require some kind of solver or iteration strategy

## Slide 51: Using solvers with implicit models
Gradient-free solver: Nonlinear Block Gauss-Seidel (i.e. Fixed point iteration)
Gradient-based solver: Newton’s Method
Lab 1: Simple aircraft sizing and experimenting with different solver algorithms

## Slide 52: OpenMDAO Nonlinear Solvers
When a circular dependency is detected, OpenMDAO needs a solver to converge the problem:
Choice #1: NonlinearBlockGS()
Choice #2: NewtonSolver()
Choice #3: BroydenSolver()
Choice #4: NonlinearBlockJac()

## Slide 53: Check out the docs for more info!
Look at the docs for OpenMDAO’s standard library:
Lots of details on all the different solvers!

## Slide 54: Check out the docs for more info!
Look at the docs for OpenMDAO’s standard library:
Lots of details on all the different solvers!
Also see sections for surrogates and helpful general purpose components!

## Slide 55: Nonlinear Block Gauss-Seidel (Gradient Free)
Inputs
Initial guess
Model 1
Model 2
Model 3
Outputs
Cycle connection

## Slide 56: Nonlinear Block Gauss-Seidel
Inputs
Initial guess
Model 1
Model 2
Model 3
Outputs
Evaluate Model 1 using initial guess inputs

## Slide 57: Nonlinear Block Gauss-Seidel
Inputs
Model 1
Model 2
Model 3
Outputs
Substitute Model 1 output into state vector and run Model 2

## Slide 58: Nonlinear Block Gauss-Seidel
Inputs
Model 1
Model 2
Model 3
Outputs
Substitute Model 2 output into state vector and run Model 3

## Slide 59: Nonlinear Block Gauss-Seidel
Inputs
Model 1
Model 2
Model 3
Outputs
Run Model 1 with input from all prior tools. Repeat until converged

## Slide 60: Nonlinear Block Gauss-Seidel
Inputs
Model 1
Model 2
Model 3
Outputs
Run Model 2 with input from all prior tools. Repeat until converged

## Slide 61: Newton’s Method is simple in one dimension (Gradient Based!)

## Slide 62: Newton Solver for multiple dimensions is a bit more complex
We want to drive residuals to 0
x: design variables
y: implicit state variables
Do a Taylor series with respect to the current point
We want residuals to be 0 at the next iteration y + dy
Solve for dy that would drive the linearize residuals to 0
But we don’t actually invert. Just solve this linear system
ny
ny
ny
1
1
=
Then take a step. Repeat from top until converged

## Slide 63: Newton Solver needs some partial derivatives!
ny
ny
ny
1
1
=

## Slide 64: Partial Derivatives in OpenMDAO
OpenMDAO assembles the Jacobian for you, from provided component partials
Define analytic derivatives:
partials(<of>, <with respect to>)
This tells OpenMDAO which partials exist
This tells OpenMDAO the actual values of the partials

## Slide 65: Lab # 1 : Aircraft Sizing
Next, we will “size” an electric aircraft for desired range
Open lab_1_template.py in a text editor or IDE and rename lab_1.py
Check the model by building an N2 diagram
This system is implicit (because it has a cycle) but has no implicit components

## Slide 66: Lab # 1 : Aircraft Sizing
Run the model as-is using NLBGS (python lab_1.py)
  The numbers that print out are the absolute and relative residuals
Change the empty weight fraction to 0.55
  check out the ExecComp
Try using the Newton solver (~ Line 124). What happens?
  Check your partial derivatives (~ Line 173)
  Fix the partial derivatives of the incorrect components
  Which solver uses fewer iterations?
Print all the inputs and outputs (~ Line 178, 179)

## Slide 67: check_partials output
------------------------- Component: ExecComp 'oew' ------------------------- '<output>' wrt '<variable>' | fwd mag. | check mag. | a(fwd-chk) | r(fwd-chk) ------------------------------------------------------------------------------- 'W_empty' wrt 'TOW' | 6.0000e-01 | 6.0000e-01 | 2.3842e-08 | 3.9736e-08 ------------------------------------ Component: BatteryWeight 'batterywt' ------------------------------------ '<output>' wrt '<variable>' | fwd mag. | check mag. | a(fwd-chk) | r(fwd-chk) ----------------------------------------------------------------------------------- 'W_battery' wrt 'LoverD' | 0.0000e+00 | 9.6353e+01 | 9.6353e+01 | 1.0000e+00 >ABS_TOL >REL_TOL 'W_battery' wrt 'TOW' | 0.0000e+00 | 3.2118e-01 | 3.2118e-01 | 1.0000e+00 >ABS_TOL >REL_TOL 'W_battery' wrt 'eta_electric' | 0.0000e+00 | 2.0946e+03 | 2.0946e+03 | 1.0000e+00 >ABS_TOL >REL_TOL 'W_battery' wrt 'eta_prop' | 0.0000e+00 | 2.3218e+03 | 2.3218e+03 | 1.0000e+00 >ABS_TOL >REL_TOL 'W_battery' wrt 'range_desired' | 0.0000e+00 | 1.2847e+01 | 1.2847e+01 | 1.0000e+00 >ABS_TOL >REL_TOL 'W_battery' wrt 'spec_energy' | 0.0000e+00 | 6.4235e+00 | 6.4235e+00 | 1.0000e+00 >ABS_TOL >REL_TOL ---------------------------- Component: WeightBuild 'tow' ---------------------------- '<output>' wrt '<variable>' | fwd mag. | check mag. | a(fwd-chk) | r(fwd-chk) ------------------------------------------------------------------------------- 'TOW' wrt 'W_battery' | 7.5000e+01 | 1.0000e+00 | 7.6000e+01 | 7.6000e+01 >ABS_TOL >REL_TOL 'TOW' wrt 'W_empty' | 7.5000e+01 | 1.0000e+00 | 7.6000e+01 | 7.6000e+01 >ABS_TOL >REL_TOL 'TOW' wrt 'W_payload' | 7.5000e+01 | 1.0000e+00 | 7.6000e+01 | 7.6000e+01 >ABS_TOL >REL_TOL ########################################################### Sub Jacobian with Largest Relative Error: WeightBuild 'tow' ########################################################### '<output>' wrt '<variable>' | fwd mag. | check mag. | a(fwd-chk) | r(fwd-chk) ------------------------------------------------------------------------------- 'TOW' wrt 'W_battery' | 7.5000e+01 | 1.0000e+00 | 7.6000e+01 | 7.6000e+01

## Slide 68: Lab # 1 : Aircraft Sizing continued
Switch back to the Gauss-Seidel solver
Switch to the WeightBuildImplicit component
  solves for TOW by forcing design range equal to analyzed range
  What happens when you run the model? Why?
  Try the Newton solver

## Slide 69: Optimization with and without analytic derivatives
High level introduction to different methods of computing derivatives
Lab 2: Optimization of a FEM for a cantilever beam

## Slide 70: Optimization
OpenMDAO is capable of evaluating DOEs just like ModelCenter, but…
Gradient based optimization is A LOT faster!
So we need total derivatives across the whole model:
??

## Slide 71: Finite difference is easy

## Slide 72: Finite difference is easy, but…
Treats your model as a black-box
Expensive
Accuracy can be bad, especially close to the optimal point

## Slide 73: Friends don’t let friends finite difference across solvers!
E. S. Hendricks and J. S. Gray, “Pycycle: a tool for efficient optimization of gas turbine engine cycles,” Aerospace, vol. 6, iss. 87, 2019.
E. S. Hendricks, “A multi-level multi-design point approach for gas turbine cycle and turbine conceptual design,” PhD Thesis, 2017.
J. S. Gray, T. A. Hearn, K. T. Moore, J. Hwang, J. Martins, and A. Ning, “Automatic Evaluation of Multidisciplinary Derivatives Using a Graph-Based Problem Formulation in OpenMDAO,” in 15th AIAA/ISSMO Multidisciplinary Analysis and Optimization Conference, 2014.
J. S. Gray, K. T. Moore, T. A. Hearn, and B. A. Naylor, “Standard Platform for Benchmarking Multidisciplinary Design Analysis and Optimization Architectures,” AIAA Journal, vol. 51, iss. 10, p. 2380–2394, 2013.
C. Marriage and Martins, J. R. R. A. “Reconfigurable Semi-Analytic Sensitivity Methods and MDO Architectures Within the πMDO Framework”, in Proceedings of the 12th AIAA/ISSMO Multidisciplinary Analysis and Optimization Conference, Victoria, BC, 2008.
Seriously… don’t do this unless you really have to.
It’s expensive (make your solver tolerances really tight)
It’s inaccurate
It will probably make your optimization converge slowly!
Lots of papers on this topic:

## Slide 74: Complex step is more accurate than FD, but…
Treats your models as a gray-box (might require code modification)
Even more expensive
Some functions are tricky…
  min(), max(), abs() can cause issues

## Slide 75: Analytic derivatives are both fast and accurate!

## Slide 76: What about models with coupling?

## Slide 77: How do you differentiate through this convergence loop?
We’ll need a nonlinear solver to converge this coupling.
The solver loop changes the way you compute analytic derivatives

## Slide 78: Manually computing analytic derivatives for coupled models takes a lot of work

## Slide 79: How do compute these extra terms?
These terms will be computed using adjoints!

## Slide 80: When models get really big … have fun!
= ???
Lets be honest, this just isn’t going to happen!

## Slide 81: OpenMDAO can compute these total derivatives for you, automatically!
= [ask OpenMDAO]
For a deep dive on the math:
[Martins and Hwang 2013]
[Hwang and Martins 2018]

## Slide 82: OpenMDAO splits total derivative computation into two steps
Computing the partial derivatives for each component
Solving a linear system for total derivatives

## Slide 83: OpenMDAO splits total derivative computation into two steps
Computing the partial derivatives for each component
  Numerical approach: FD/CS
  Analytic approach: hand derivation or algorithmic differentiation
  Mix and match numerical and analytic
You are responsible for this step, but OpenMDAO can help you a bit

## Slide 84: OpenMDAO splits total derivative computation into two steps
1) Computing the partial derivatives for each component
2) Solving a linear system for total derivatives OpenMDAO does this automatically using a library of different linear solvers for different problems

## Slide 85: By using OpenMDAO’s analytic derivative functionality you can
Efficiently solve optimization problems with 1000’s of design variables or thousands of constraints
Get total derivatives across a complicated model, by providing only partial derivatives of each component
Mix and match different techniques for computing partial derivatives

## Slide 86: Rules of thumb for computing partials
Fine to start out with FD partials while getting your model set up!
For cheap black-box codes:
  FD might be ok for production runs
  CS is better if you can do it!
For “expensive” codes (anything with an internal solver):
  Implement as ImplicitComponent (expose the states/residuals to OpenMDAO)
  Can still FD the residual if you need to
  Analytic derivatives typically cost a lot for these components

## Slide 87: Optimization
Optimization is handled by a Driver
add_objective(<var_name>)
add_design_var(<var_name>, lower=…, upper=…)
ScipyOptimizeDriver is what most people will use on Windows
run_driver instead of run_model
add_constraint(<var_name>, lower=…, upper=…)
# build the modelprob = om.Problem()
indeps = prob.model.add_subsystem('indeps', om.IndepVarComp(), promotes=['*’])
indeps.add_output('a', .5)
indeps.add_output('Area', 10.0, units='m**2’)
indeps.add_output('rho', 1.225, units='kg/m**3’)
indeps.add_output('Vu', 10.0, units='m/s’)
prob.model.add_subsystem('a_disk', ActuatorDisc(),
promotes_inputs=['a', 'Area', 'rho', 'Vu’])
# setup the optimization
prob.driver = om.ScipyOptimizeDriver()
prob.driver.options['optimizer'] = 'SLSQP’
prob.model.add_design_var('a', lower=0., upper=1.)
prob.model.add_design_var('Area', lower=0., upper=1.)
# negative one so we maximize the objective
prob.model.add_objective('a_disk.Cp', scaler=-1)
prob.setup()
prob.run_driver()

## Slide 88: Optimization
Available drivers:
ScipyOptimizeDriver will work in Anaconda
  Works on Windows machines
  SLSQP method is the standard constrained opt in OpenMDAO
PyoptSparseDriver is much better (SNOPT algorithm) but really only builds on Linux/MacOSX

## Slide 89: Recording the optimization history
Often you will want to record variable values changing over the course of an optimization.
This is achieved using a “recorder” object
This will record all the objective, all constraints, and all dvs for each optimizer iteration (but no “intermediate variables”)

## Slide 90: Saving all the variables for the final optimized point
We don’t normally save all the variables for every iteration to avoid making huge database files
This configures a secondary case type to record specific runs with all the variables

## Slide 91: Lab #2: Optimization of a cantilever beam
Find the thickness distribution for a cantilever beam that minimizes compliance subject to a volume constraint
Check out the other examples on your own!
F

## Slide 92: Lab #2: Simple FEM in 5 steps!
0) Break the beam into segments (0 doesn’t count as a real step!)
Compute the moment of inertia for each segment
Compute the local stiffness matrix for each segment
Combine all the local stiffness matrices into a global K matrix and solve the FEM
Pull displacements from the state vector and compute compliance
Compute beam volume

## Slide 93: Lab #2: Pay close attention to step 4!
0) Break the beam into segments (0 doesn’t count as a real step!)
Compute the moment of inertia for each segment
Compute the local stiffness matrix for each segment
Combine all the local stiffness matrices into a global K matrix and solve the FEM
Pull displacements from the state vector and compute compliance
Compute beam volume
using the src_indices argument to the connect method,
you can extract just the relevant portion of the state vector for the
compliance calculation

## Slide 94: Lab #2: Get to it!
Copy the “lab_2_template.py” file to a new file called “lab_2.py”
Add components in the correct order (~ line 40)
Connect the components together (~line 48)
Use the N2 diagram to make sure you have everything connected (no red inputs!)
What happens if you switch to full model FD? Does it work? Try changing the FD step size…
What about CS?
How does compute cost scale with num_elements for different methods of computing derivatives?

## Slide 95: Wrapping external codes
How to handle file wrappers with OpenMDAO built in helper components
Lab 3: Explicit and Implicit file wrappers

## Slide 96: OpenMDAO has two file wrapper components in the standard library
There are lots of useful components
In the standard library!
spines, constraint aggregation,
file wrappers, Ax=b, Ax, etc…
Have a look through these comps,
So you know whats there

## Slide 97: ExternalCodeComp
Inherit from OpenMDAO provided class
Define the I/O like normal
Wrapper specific options
Write the input file
Create a sub-process to run the code
Parse the output file
Push the values back into
OpenMDAO’s output vector

## Slide 98: ExternalCodeImplicitComp
Inherit from OpenMDAO provided class
(different base class then for the explicit case!)
Define the I/O like normal
apply_nonlinear is the
Residual evaluation
Write the input file
Create a sub-process to run the code
Parse the output file
Wrapper specific options
solve_nonlinear asks the
code to converge itself using
its own internal solvers

## Slide 99: Lab #3: Beam optimization with file wrapped external codes
cd into the `lab_3` folder
Have a quick look at standalone_beam.py this is a pure python version of the same FEM you built in OpenMDAO for Lab #2 (but without derivatives)
Call `python standalone_beam.py opt` from the command line
Call `python lab_3_explicit_wrapper.py`
Call `python lab_3_implicit_wrapper.py`
Why does the implicit wrapper call both solve_nonlinear and apply_nonlinear? (hint: it has to do with derivatives)
Compare the compute cost of running the optimization using pure OpenMDAO, the standalone optimization, and the file wrapped version.

## Slide 100: Advanced Topics
Vectorization
Model architecting
DevOps
Surrogate modeling
High-fidelity and expensive tools
Trajectory optimization
Propulsion analysis

## Slide 101: Vectorization
Where possible, avoid instantiating models over and over for multi-point analyses (e.g. trajectory optimization)
Instead, do vectorized computations using numpy
OpenMDAO needs to know the dimension of all component inputs / outputs at setup() time
  Best practice: pass in vector length as a self.option[‘vec_size’]
  If you mess this up you’ll get dimension mismatch errors at run time

## Slide 102: Vectorization
shape=(dim1, dim2,…)
User sets vector dims when instantiating the model
Sparse Jacobian indices for vector input and vector output
Sparse Jacobian indices for scalar input and vector output

## Slide 103: Vectorization
Many flight conditions computed at once using vectorized computation

## Slide 104: Dealing with complex models
Developing good OpenMDAO models is like object-oriented software engineering: you need to pick the right level to draw the component boundary
In my opinion, a good component has:
  on the order of 5 – 20 inputs
  1 – 20 outputs
  a few computations that are logically related
Python’s package import system makes this easy
Example: https://github.com/mdolab/openconcept